Use Neural Circuit Policy for autonomous navigation

Introduction:

End to end learning has been widely applied to autonomous driving research field in recent years and achieved outstanding performance as traditional structured approach. The benefit of the learning method is people don’t need to spend large amount of time to tune the models, such as tuning the parameters in control systems. However, large deep neural network has its internal unknowns. Since the neural network is huge, people can’t know what happens in each stage. This black box method raises the concerns of safety issue. How can the researchers guarantee the safety without knowing how their network works? Researchers from MIT provided the potential solution for this issue and make end to end learning approach feasible for human to understand. They came up with the neural circuit policy inspired by the brain from C-elegans. Briefly, the learning algorithms will contain four layers called: Sensory, Inter-neuron, Command and Motor. Neurons. They are not fully connected with each other but with the special connections with respond to c-elegan’s brain. Our group use this learning algorithm to make Jackal, which is a four wheeled robot, to run autonomously. The navigation tasks consists line following and obstacle avoidance.

Design:

We separate our tasks into two phases. Phase1 aims for obstacle avoidance. We use Velodyne 3D Lidar to be the input of our system for detecting the obstacle. We read its Laser_scan to map the obstacles around. We design our learning algorithm by using convolutional neural network(CNN) modules and neural circuit policy (a control system of the model). Our system is separated into two parts: image processing and control. We use CNN to extract structural features from the Laser_scan data. Based on this scan information, the network decides to pass the useful scans into the control system. This control system uses neural circuit policy, which steers the vehicle using the decisions made by a set of biologically-inspired neurons. It translates the data from the compact convolutional model outputs to only 21 control neurons in an RNN structure and output angular or linear velocities.

Phase2 aims for line following task. We equipped realsense camera on the Jackal and output RGB image data as input to our learning system. We use the same learning system as we constructed for obstacle avoidance, which is CNN plus NCP model. The input to the whole system is RGB data and output is control commands, which are angular velocities.

Hardware Experiment

Phase1(obstacle avoidance):
We set our experiment field using trash bins and chairs as obstacles. Our goal is to use our trained model to make Jackal detect and go around these obstcales. Jackal don’t have any destinations, so we put the Jackal directly in front of a chair to start.

We first manually run Jackal through obstacles using slam tool box on Robot Operating System(ROS) to collect laser scan messages, linear and angular velocities. We trained linear and angular velocities separately paired with the same scan message data. One training model will give us predicated angular velocity using scan message and collected angular velocity as training inputs. Another training model will give us predicated linear velocity using scan message and collected linear velocity as training inputs. After having those two trained models, we constructed ROS node (load_model) to publish predicated linear and angular velocity into cmd_vel topic, which controls the forward speed and steering speed of Jackal.

Training results:

Phase2(line following)
We use blue tape to construct an L-shaped-road. Our goal is to demonstrate our trained model can follow the line from the start to the end of the road.

We first manually run Jackal through the road using keyboard control. After collecting five rounds data, we input collected RGB data and angular velocity into our training model and output predicated angular velocity. All input images are processed; blue color is extracted and images are converted to gray scale. Such way, the line is more obvious to the model during training. We didn’t collect linear velocity since we stabilize our linear velocity when manually run the Jackal. When we test our model, we use the same linear velocity. We constructed ROS nodes to publish predicated angular velocity on cmd_vel topic.

Training results:

Testing Results and discussion:

Our experiment results for both phases are quite successful. For obstacle avoidance task, Jackal successfully get around the trash bins. Since it didn’t have a clear goal, after avoiding the obstacle, it will run without a clear direction.

For line following task, Jackal successfully follow the line from the start to the end. But it runs need to run quite slow because the frequency of camera output its data is around 1.1 and 1.2 Hz. If Jackal run fast, it can’t see the line and will lost its direction.

In the future, we can combine those two tasks into one single task, which will need to find a way to incorporate RGB and Lidar data or learned how to use those two trained models together. Since we have two trained models and both of them will publish angular velocity for now, we need to consider cases that one need to stop publish and let the other one to publish angular velocity. For example, we uses camera to detect colored lines on both sides and use them as constricts. If Jackal stays between, ask obstacle avoidance model to publish angular and linear velocity. But if Jackal runs out of the lines, ask line following model to drag Jackal back to the road. Camera frequency issue need to be fixed as well if we want the Jackal runs more frequently. We may choose a different camera or tried to change its publish frequency.

Conclusion:

We achieved such performance using only 21 control neurons. Such small amount give us opportunity to understand the functions of each stage as we did in our traditional structured control approach. This also gives use safety pipelines. We can evaluate the safety of the whole driving system in a more concrete way but not just from the probability of the testing data. By addressing this safety issue, end to end learning can be widely used on the road and acceptly by the market.